## Slide 1: Experimental Determination of the Parameters of the Liquid Infiltration into the Sand
Volodymyr Oliinik
Olesya Slavhorodska
3rd Fire Engineering & Disaster Management Prerecorded International Scientific Conference Védelem online – cooperated with the University of Public Service 26 April, 2023, Budapest, Hungary

## Slide 2: About the Authors
Volodymyr Oliinik
E-mail:
oleinik@nuczu.edu.ua
Olesya Slavhorodska
E-mail:
slavgorodskaya05092017@gmail.com
Candidate of technical sciences, Associated Professor, Head of department of Fire and Technogenic Safety of Facilities and Technologies National University of Civil Defence of Ukraine, Kharkiv, Ukraine
Cadet National University of Civil Defence of Ukraine, Kharkiv, Ukraine

## Slide 3: Abstract
Based on the Green-Ampt model we plotted the curve to show the dependence between the time and the depth of the liquid infiltration into the loose material. This curve was obtained by solving the system of differential equations. One of these equations describes a decrease in the surface liquid layer thickness and the other equation describes the in-depth infiltration dynamics. The logarithmic function expansion into series allows us to turn from the irrational expression to the approximating polynomial. Polynomial coefficients are defined by the least square method. Using as an example the infiltration of the raw oil into the sand we showed that the polynomial with the addends of the second and third orders satisfactory approximates the specified dependence of the infiltration time on the infiltration depth. In this case, the approximation error is within 10% after the first minute of the accidental spill. A linear character of the relationship between the thickness of the liquid layer spilled on the sand surface and the infiltration depth enables the evaluation of the statistical parameter of infiltration, i.e. the porosity factor.

## Slide 4: Introduction
Many emergency situations that arise in chemical and recycling industries, including the transport originate due to the accidental spread of flammable or other unsafe liquids [1]. The infiltration of liquid into the ground results in the contamination of water resources, in particular underground waters [2] and river waters [3]. However, the ignition of the flammable liquid presents the greatest danger. It threatens with the spread of fire to neighboring industrial facilities and natural landscapes and it also results in the discharge of contaminating substances into the atmosphere [4]. Spreading at large distances, these substances essentially affect the air state and create certain risks for the population [5].
Paper [6] analyzes the risks relating to the transportation of dangerous cargoes by railway. In spite of the available normative documents that govern fire safety regulations for the transportation of dangerous cargoes the latter sometimes cause emergency situations. It is confirmed by extraordinary situations caused by the spread or combustion of flammable liquids not only on the railways in Ukraine but also worldwide according to the latest events.
2021 (the USA, Texas) the train carrying oil products went off the rails and hit the truck. Three tank cars caught fire, the flame height attained several tens of meters. The people living in the neighborhood were evacuated.
2020 (the USA, Arizona) oil tanks with highly flammable liquids went off the rails and inflamed.
2020 (Kazakhstan, Zhambil region) the petroleum tank car went off the rails, the liquid was spilled and inflamed. The fire caught the area of nearly 600 m2..
2019 (Canada, Manitoba) the train carrying 37 oil tanks went off the rails and the oil was partially spilled.

## Slide 5: Objective/Methods
The analysis of the models of the spread of combustible liquids proved that they do not take into account the penetration of the liquid into the underlying surface. This, in turn, leads to errors in estimating the size of the spill and the dynamics of its formation. Liquid seepage into bulk material, in particular, soil, is described by the Green-Ampt model [1]. The model considers the boundary between dry and already wet soil. For conducting experimental studies, sand was used as bulk material, which was poured into a cylinder with a diameter of 60 mm. Crude oil was chosen as the liquid. The results of measuring the depth of impregnation, the thickness of the liquid layer on the surface at different moments of time are given in [2]. The relationship between the thickness of the oil layer on the surface of the sand and the depth of impregnation is almost linear (Fig. 1).

## Slide 6: Objective/Methods
Fig. 1. Infiltration of the liquid deep into the ground: 1- the surface liquid; 2 –wetted ground; 3 – dry ground
0
h0
z
1
2
3
z
The infiltration of liquid into the loose material, in particular ground is described by Green-Ampt model [7]. The model gives consideration to the boundary between the dry and wet grounds. The infiltration of the liquid in-depth of the ground results in the shift of this boundary downward. Let’s orient the vertical axis Z making it to coincide with the infiltration vector (Fig.1).

## Slide 7
Then, the infiltration rate can be expressed as:
The infiltration rate is described by the Darcy’s law
where К is the hydraulic conductivity of the wetted ground and is the hydraulic gradient:
ho is the liquid layer thickness on the ground surface; z is the wetted ground layer thickness;
hf is the capillarity value.
By combining the expressions (1) and (3) we obtain the equations
The infiltration of the liquid deep into the ground results in a decreased layer thickness on its surface:
Solving the equation system (4)-(5), we will obtain the dependence of the infiltration time on the infiltration depth z.

## Slide 8
The dependence of the time of impregnation of crude oil into sand on the depth of impregnation is approximated by a polynomial containing terms of the second and third powers relative to the depth of impregnation z. The analysis of the impregnation of crude oil into sand shows that the depth of impregnation and the thickness of the liquid layer on the surface of the sand are linearly related. In fig. 2 shows the experimental dependence of time on the depth of impregnation and its approximation in the form:
We will look for unknown coefficients a, b as values that ensure the minimum of the sum of squares of the deviations of the time values t(zn) calculated by the formula from the experimental values tn:
Fig. 2. Relationship between the oil layer thickness on the sand surface and the infiltration depth
Fig. 3. Dependence of the infiltration time on the infiltration depth: 1-experiment; 2-approximation in the form of (6)

## Slide 9: Findings/results
The system of differential equations that describe the liquid spread on the sloped surface, the depth infiltration and the liquid burnout has been constructed. In addition, the availability of the surface asperities that should be filled by the spilled liquid was also taken into account. The spread type, i.e. instantaneous or continuous was taken into account in initial conditions. The method of finite elements was used for the solution of the equation system.
The developed algorithm enables the definition of the spread area, the dynamics of its change and the liquid layer thickness.

## Slide 10: Conclusion/suggestions
Based on the Green-Ampt model, we can suggest the method for the determination of the parameters of the liquid infiltration into the loose ground. Solving the system of differential equations with one equation describing the liquid layer thickness on the ground surface and the other equation describing the in-depth infiltration dynamics we obtain the relationship between the infiltration time and infiltration depth. The expansion of the logarithmic function into series enables the replacement of the obtained irrational relationship with the approximating polynomial. To estimate polynomial coefficients we used the least-square method that leads to the minimization problem that has the unique solution.
The dependence of the time of infiltration of the raw oil into the sand on the infiltration depth was approximated by the polynomial that includes the addends of the first and third orders with regard to the infiltration depth z.A relative error of such approximation is within 10% after the first minute of spreading.
The analysis of the infiltration of the raw oil into the sand shows that the infiltration depth and the liquid layer thickness on the sand surface have a linear relationship. It allows us to estimate the value of the static parameter of the infiltration, i.e. the porosity coefficient. The experimental value of it is 0.314.

## Slide 11: References
Raja, S., Tauseef, S. M., Abbasi, T.: Risk of Fuel Spills and the Transient Models of Spill Area Forecasting. Journal of Failure Analysis and Prevention 18, 445–455 (2018).
Sadkovyi, V., Pospelov, B., Andronov, V., Rybka, E., Krainiukov, O., Rud, А., Karpets, K., Bezuhla, Y.: Construction of a method for detecting arbitrary hazard pollutants in the atmospheric air based on the structural function of the current pollutant concentrations. Eastern-European Journal of Enterprise 6/10(108), 14–22 (2020).
Rybalova, O., Artemiev, S., Sarapina, M., Tsymbal, B., Bakhareva, A., Shestopalov, O., Filenko, O.: Development of methods for estimating the environmental risk of degradation of the surface water state. Eastern-European Journal of Enterprise Technologies 2/10(92), 4–17 (2018).
Mygalenko, K., Nuyanzin, V., Zemlianskyi, A., Dominik, A., Pozdieiev, S.: Development of the technique for restricting the propagation of fire in natural peat ecosystems. Eastern-European Journal of Enterprise Technologies 1(10), 31–37 (2018).
Kustov, M. V., Kalugin, V. D., Tutunik, V. V., Tarakhno, E. V.: Physicochemical principles of the technology of modified pyrotechnic compositions to reduce the chemical pollution of the atmosphere. Voprosy khimii i khimicheskoi tekhnologii, 1, 92–99 (2019).
Pospelov, B., Kovrehin, V., Rybka, E., Krainiukov, O., Petukhova, O., Butenko, T., Borodych, P., Morozov, I., Horbov, O., Hrachova, I.: Development of a method for detecting dangerous states of polluted atmospheric air based on the current recurrence of the combined risk. Eastern-European Journal of Enterprise 5/9 (107), 49–56 (2020).
Meel, A., Khajehnajafi, S.: A comparative analysis of two approaches for pool evaporation modeling: Shrinking versus nonshrinking pool area. Process Safety Progress 34, 304–314 (2012).

## Slide 12: THANK YOU FOR YOUR ATTENTION! Email address of the authors oleinik@nuczu.edu.ua